## Slide 1: Baker Creek Driving Data Preparation Methodology
By Haley Brauner

## Slide 2: Air Pressure
Compared Vital, Yellowkinfe A, and GEM @ Vital datasets
    Yellowknife is consistently greater than the other 2 locations
    Vital and GEM @ Vital match almost perfectly except that in 2009, Vital is shifted forward by 6 days (shifting back 6 days matches almost perfectly
Combining methodology:
  Used Vital data primarily, with the 2009 observations shifted back in time by 6 days
  Gap-filled with GEM @ Vital data
  The following 2 slides show a comparison of the original and shifted data, followed by the 2012-2018 data and the a close-up of just 2009 (shifted)

## Slide 3
Notes: Vital matches closely with GEMVital (where present)
Note the 6-day shift in 2009

## Slide 4
Notes: - Shifting the 2009 data by 6 days makes the data match up nearly perfectly

## Slide 7: Air Temperature
Combining methodology:
  A dry adiabatic lapse rate of 6.5oC/km was used to scale the Vital observations at 2.8 m (incorrectly labelled as 1.1m) and 4.4m, and Yellowknife A (2 m) up to 40 m
  The shift in 2009 Vital data was also present and was shifted back by 6 days to match
  Vital at 4.4 m was used as the primary dataset, then gap-filled with Vital at 2.8 m, followed by Yellowknife then GEM data
The following slides show a comparison of the datasets for 2005-2011, including before and after the shift in Vital data

## Slide 11: Incoming Shortwave Radiation
When comparing the data, noticed a magnitude shift upward in the Vital data starting around June 21, 2008
Noticed that in 2009, the Vital data seems to be shifted forward by 3 days (not 6 like the other variables)
In 2016, daily average values look to be too high at the Vital station
Combining methodology
  Vital was used as the primary, but omitted 2008 from June 20 to the end of the year, 2016 prior to April 17, and shifted 2009 back by 3 days
  Gap-filled with Landing data
  Gap-filled remaining with GEM @ Vital was used to gap-fill
  Negative values were later converted to zero in Excel prior to being used in the model

## Slide 17: Incoming Longwave Radiation
Compared GEM and Vital data
    In 2005, there were minimal Vital observations
    In 2008, the June and July data was shifted upward, and a fair number of large negative values in July
    The 2009 Vital data appeared to be shifted forward by 3 days
Combining Methodology:
  Used Vital as primary data but filtered out June 20, 2008 onward and shifted 2009 back by 3 days
  Gap-filled with GEM data

## Slide 21: Humidity
During the summer months, GEM @ 2m  GEM @ 40 m < Vital (both 2.8 m and 4.4 m), < Yellowknife < Landing
    Since the Landing tower is at a lake, humidity is expected to be higher
In the winter, Yellowknife q is approximately equal to the GEM data
Tried scaling Vital and Yellowknife summer observations up to 40 m by using the T@40m instead of T near ground; didn’t make much of a difference
Combining Methodology:
  Used the observed values from Vital @ 4.4 m as the primary (knowing that in the summer, the values are likely biased low.
  Gap-filled with GEM (@40m) data

## Slide 25: Wind Speed
Scaled wind speed up to 40 m using equations 3.27 and 3.30 a and b
Observations of Vital match reasonably well with GEM @ 40m, and Yellowknife seems to be lower. Could be due to rain interference or lower sensitivity instrument, but also there were many zero values in the hourly data. Therefore, Yellowknife not used
Combining Methodology
  Used scaled Vital with 2009 shifted back 6 days as the primary
  Used GEM @ 40 m (Vital) to gap-fill

## Slide 29: Precipitation
Combining methodology:
  Used Vital as primary (shifted 2009 back by 6 days again)
  Gap-filled with CaPA @ the Vital location
Note that looking at the annual cumulative bar graph (3 slides ahead), sometimes the combined precip is greater than CaPA, and sometimes less; this is due to the differences between the observed Vital data and the CaPA dataset