## Slide 1: Representation of Spatial Heterogeneity in the MESH Model MWS Capstone Project Presentation August 23, 2019 A project in partnership with Environment and Climate Change Canada

## Slide 2
Representation of Spatial Heterogeneity in the MESH Model
School of Environment and Sustainability
Agenda
Problem Statement
Methods and Results
  Site familiarization
  Data preparation
  Modelling
Findings
Proposed Solution
Notes: I will discuss the goals of the project, methods and results used in each stage, the main findings, and proposed solutions

## Slide 3: What were the goals of the project?

## Slide 4
Baker Creek
White Gull Creek
In the Baker Creek watershed, replicate the MESH modelling methodology used in 2017 in the White Gull Creek watershed
Take the work further
  More grid cells
  Different runoff algorithm
?
Evaluate model performance
Project Goals

## Slide 5: What is MESH?

## Slide 6: M Modélisation E Environmentale communautaire S Surface and H Hydrology
What is MESH?
LSS
Specific Processes
Runoff
Routing
GEM
University of Saskatchewan, 2019 (Haghnegahdar, Tolson, Craig, & Paya, 2015)
Notes: MESH is Environment and Climate Change Canada’s land surface hydrology model. It is a community system – open-source and continually being developed
MESH is comprised of:
A Land Surface Scheme, which takes care of the vertical water and energy balances
Runoff algorithms
Various representations of other hydrological processes, such as infiltration into frozen soil, groundwater, and baseflow
And routing
One of the benefits of MESH is the ability to do comparative studies by swapping out one land surface scheme for another, or changing the runoff mechanism, such as WATROF and PDMROF
MESH can either be coupled with an atmospheric model such as GEM, or run offline

## Slide 7: Site Familiarization

## Slide 8
Site Familiarization
Yellowknife
Spence & Hedstrom, 2018; Phillips, Spence, & Pomeroy, 2011
Methods
  Papers
  Photos and maps
  Talking to Chris Spence
Results
  Climate
    Subarctic
    Short, cool summers and long, cold winters
    Average 289 mm precipitation, 41% snowfall
  Geology and Soils
    Precambrian Shield (bedrock)
    Pockets of glaciolacustrine and weathered bedrock deposits
    Overburden thickness ranges from <1m to >10m
    Peat and organic matter ranges from thin layer on hillslopes to 1.2 m in peatlands
Notes: In order to familiarize myself with the site, I read publications, looked at photos and maps, and talked to Chris, who has done extensive research in the basin
Baker Creek is located in the Northwest Territories, just north of the capital city of Yellowknife and near Great Slave Lake. The climate is characterized as subarctic, with short, cool summers and long, cold winters. The basin receives about 290 mm of rain, on average, 41% of which is snowfall.
The basin is located in the Precambrian shield, and overburden thickness can be 10m thick or more. A layer of peat covers all deposits, with thicknesses ranging from 20cm to over a meter.

## Slide 9
Site Familiarization
WSC Gauge
Spence & Hedstrom, 2018; Phillips, Spence, & Pomeroy, 2011; Spence, 2006
Hydrology
  349 Lakes; Large lakes dominant
  Flow regime is highly variable due to variable storage and release
    Soil storage
    Infiltration capacity
    Bedrock fractures
    Rainfall intensity
    Evaporation
    Discontinuous permafrost
    Backflow
  Contributing area and “gatekeepers”
  Spring snowmelt runoff peaks, smaller fall peaks
  Wet period: 2008-2012; Dry period: 2012-2016
Notes: The hydrology of the basin is dominated by large lakes connected by short streams. The outlet, defined by a water survey of Canada gauge at the outlet of lower martin lake, experiences a highly variable flow regime due to variable storage and release in the basin. The large lakes and other elements act as “gatekeepers” and the contributing area is highly variable. The annual hydrograph shows spring snowmelt runoff peaks, and smaller fall peaks. However, streamflow is a very small portion of the total rainfall, with runoff ratios of 0.17. During the modelled period, there was a wetter-than-normal period, followed by drier-than-normal.

## Slide 10
Site Familiarization
Spence & Hedstrom, 2018; Cook, 2019; Guan, Spence, & Westbrook, 2019
Vegetation and Landcover
Photo credit: A. Cook, 2019
Notes: The main landcover types in the basin are shown here, and you can see bedrock in the foreground, short open forests, with a large lake and coniferous forested hillslopes in the background.
Again, bedrock, a lake, and forested hillslopes.
This is a wetland area, which flows into Vital Lake
This is an example of peatland, which are large peat-filled depressions with short shrub cover and some jack pines

## Slide 11: Data Preparation

## Slide 12
Data Preparation
Spence & Hedstrom, 2018; ECCC, 2014
Methods
  Combine several different datasets
    Unit conversions, timezone shifts, interpolation, measurement elevation shifts up to 40m,
    1 continuous dataset
  All using R
  QA/QC
    Graphical comparison
    Conservation of mean or sum
Results
  Continuous set of forcing data for the modelling period for 7 hydrometeorological variables
GEM and CaPA
Vital Tower
https://www.cbc.ca/news/canada/north/yellowknife-airport-fees-take-toll-air-north-1.4482135
Notes: Data preparation was a significant chunk of my project. I combined data from three different sources – a research tower on site, Environment Canada station at Yellowknife, and the environment Canada climate model datasets.
I performed unit conversions, timezone shifts, interpolation, and measurement elevation shifts up to 40m – the reference height for the model.
All was done using R, and I also QA/QC’d the data
At the end, I had a continuous set of forcing data for the modelling period for 7 hydrometeorological variables.

## Slide 13: Modelling

## Slide 14
Modelling
Hossain et al., 2016; Spence & Hedstrom, 2018; Mkandla, 2017;
Methods
3 Phases
  Phase 1: replicate White Gull Creek methodology (S1 & S2)
  Phase 2: Increase complexity by adding more grids (S3)
  Phase 3: PDMROF (S1-P and S2-P)
Calibration and Validation
  1 year spin-up: Fall 2006-2007
  5 years calibration: Fall 2007-2010 & 2013-2015
  4 years validation: Fall 2010-2013 & 2015-2016
Parameterization and initial conditions
  From the literature – Baker Creek and other MESH modelling
  First-hand knowledge of the watershed
Calibration
  OSTRICH program
  1000 iterations for 100 trials
    Ran in batches to reduce total run time
  Nash-Sutcliffe objective function
Lumped
Semi-distributed
Notes: Modelling was conducted in 3 phases. Phase 1 was a replication of the methodology used for modelling the White Gull Creek basin which included Scenario 1 and 2. The main difference is that Scenario 1 had 1 GRU and 2 had 6 GRUs. A GRU is a subset of the watershed that is expected to behave hydrologically similary. For phase 2 (scenario 3), I increased the complexity of the model by adding more grid cells, and in Phase 3 I repeated Scenarios 1 and 2 using a different runoff algorithm, PDMROF, which incorporates a variable contributing area (fill-and-spill)
I had a 1 year spin-up for the model, calibrated to two different periods (1 wet and 1 dry), and then validated the model against the remaining wet and dry years.
I parameterized the model using published literature about Baker Creek and MESH modelling in other areas, as well as by talking to Chris about the watershed.
Calibration was run using the Ostrich program with 1000 iterations per trial and 100 trials. Nash-Sutcliffe was used as the objective function.

## Slide 15
Modelling
Mkandla, 2017
White Gull Creek Watershed
1
1
Uniform
2
1
Distributed
Uniform
2
2
Distributed
Uniform
10 (5x2)
10
Distributed
1
2
3
4
5
6
GRUs
Parameter Sets
Forcing Data
Baker Creek Watershed
1
1
Uniform
6
6
Uniform
GRUs
Parameter Sets
Forcing Data
Notes: This is a quick comparison of the model configurations for White Gull Creek and Baker Creek. Due to only one ecodistrict and 1 set of driving data in Baker Creek (also, the watershed was about ¼ the size), I only had 2 scenarios instead of the 6 in the original study.

## Slide 16
Modelling
Results
NSE =
Scenario 1 < Scenario 2 < Scenario 3
PDMROF performed better than WATROF
Streamflow
  Most spring peaks modelled
    Under-estimated in wet period, over-estimated in dry period
  Fall peaks missed in S2, some shown in S2-P
Notes: The first very obvious result was that the NSE values were very poor. However, there are still some meaningful trends. As the model complexity increased from scenario 1 through 3, so did the performance. Also, PDMROF performed better than WATROF in both cases. Looking at the comparison hydrographs, the spring peaks were captures, but they were underestimated in the wet period and over-estimated in the dry period. Fall peaks were missed in Scenarios 1 through three, but showed up in Scenario 2-P.

## Slide 17
Modelling
Mkandla, 2017
Run time
Calibration vs Validation NSE
Notes: I also found that the Run time increased with increasing complexity, with a significant difference between scenarios 2 and 3. A 262% increase in run time resulted in only marginal performance improvement.
Also, PDMROF took longer than WATROF
In every scenario except 1-P, the validation NSE was lower than calibration.
Increased with increasing complexity
25.8 hrs and 262% difference between scenarios 2 and 3
Marginal NSE increase from 2 to 3
PDMROF took longer than WATROF
  49% longer (S1) and 26% (S1)
Cal vs Val NSE
Lower for all (<0 in fact) except Scenario 1-P
Identifiability:
Degree to which the “true” value can be obtained by the model
1 identifiable parameter in Scenario 1
3 in Scenarios 2 and 3
2 for Scenarios 1-P and 2-P

## Slide 18: Summary of Findings Proposed Solutions

## Slide 19
Peak flows underestimated during wet period and over-estimated during dry period
  Calibration tried to match both, and did a poor job of both
  Using NSE as the performance metric favored peak flows
  Poor representation of bedrock
    Model sends runoff directly to the stream, when in reality water is stored in fractures, wetlands/peatlands in the upland areas, in the large lakes before showing up as streamflow. Or, it is held in small depressions and evaporated/transpired
  Recommendations:
    Try calibrating to just during the wet period and/or during the dry period
    Try using NSE of the log of the flows
    Try calibrating to another measurement, such as ET and/or snow depth
    Improve bedrock representation, either explicitly or effectively
Under-representation of fall peak flows
  The model is not representing key hydrological process(es) that control elevated fall flows
  PDMROF showed some higher fall flows (esp. 2009 and 2010) since it has a better representation of storage and release in the basin
  Recommendations:
    Improve the representation of the threshold functions of elements on the landscape (i.e. peatlands, wetlands, large lakes)
    Try calibrating to the fall peaks
Summary of Findings, and Proposed Solutions

## Slide 20
Very poor NSE results for all scenarios
  Potentially an issue with 1 or more parameters or ranges
  Could also be an issue with the initial soil moisture / temperature values, and/or thermal properties of the soil layer configuration
  Recommendations:
    Take another look at the parameters to try and identify where improvements could be made; perform a sensitivity analysis to assist with this
    Initialize the soil moisture and temperature conditions with an iterative spin-up period
    Change the layering and/or depth of the soil layers (Elshamy et al, 2019) since discontinuous permafrost location
Summary of Findings, and Proposed Solutions

## Slide 21: Personal Reflection

## Slide 22
Personal Reflection
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-NC
MESH
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY
This Photo by Unknown Author is licensed under CC BY-SA
Notes:   How long to struggle through things before asking for help
  The importance of taking constructive breaks even when there is lots to do

## Slide 23
Bruce Davison and Environment and Climate Change Canada for putting forward this project and for guidance, direction, and encouragement along the way
Dan Princz (ECCC) for invaluable training and assistance in running the model, and overall MESH knowledge – I couldn’t have done it without you!
Chris Spence for imparting his first-hand knowledge of the basin
Andrew Ireson, for providing direction at the start of the project, training in Linux and R, and support during the project
Kevin Shook, for providing an R training session
Ines Sanchez, for assistance with using ArcMap
Amy Cook for the photos from the basin
A great big THANKS! goes out to…

## Slide 24
Thank You!

## Slide 25
References
Cook, A. (2019). Photographs in the Baker Creek Watershed. Northwest Territories, Canada.
Environment and Climate Change Canada. (2014, October 29). Regional Deterministic Precipitation Analysis (RDPA-CaPA). Retrieved from http://collaboration.cmc.ec.gc.ca/cmc/cmoi/product_guide/docs/lib/capa_information_leaflet_20141118_en.pdf
Guan, X. J., Spence, C., & Westbrook, C. J. (2010). Shallow soil moisture - Ground thaw interactions and controls - Part 2: Influences of water and energy fluxes. Hydrology and Earth System Sciences, 14(7), 1387–1400. https://doi.org/10.5194/hess-14-1387-2010
Haghnegahdar, A., Tolson, B. A., Craig, J. R., & Paya, K. T. (2015). Assessing the performance of a semi-distributed hydrological model under various watershed discretization schemes. Hydrological Processes, 29(18), 4018–4031. https://doi.org/10.1002/hyp.10550
Hossain, K, Elshorbagy, A., Bharath, R., Davison, B., & Wheater, H. S. (2016). A Comparative Study of the Runoff Generation Algorithms in MESH Hydrological Model, (May).
Mkandla, H. (2017). Representing Spatial Heterogeneity for the White Gull Creek Watershed using the MESH model. University of Saskatchewan, Global Institute for Water Security. Saskatoon: School of Environment and Sustainability.
Spence, C. (2006). Hydrological processes and streamflow in a lake dominated watercourse. Hydrological Processes, 20, 3665–3681. https://doi.org/10.1002/hyp
Spence, Christopher, & Hedstrom, N. (2018). Hydrometeorological data from Baker Creek Research Watershed, Northwest Territories, Canada. Earth System Science Data, 10(4), 1753–1767. https://doi.org/10.5194/essd-10-1753-2018
University of Saskatchewan. (2019a, August 7). About MESH. Retrieved from MESH - A Community Hydrology-Land Surface Model: https://wiki.usask.ca/display/MESH/About+MESH
Representation of Spatial Heterogeneity in the MESH Model